## Slide 1
PROJECT TITLE
Design & Verification of a 32-Bit RISC-V Single-Cycle Processor (RV32I)
Complete Verilog HDL implementation with hierarchical decoding and cycle-accurate verification
Presenter
Prince Raj Computer Architecture & Digital System Design
Implementation Details
• Language: Verilog HDL (IEEE 1364) • ISA: RISC-V RV32I Base Integer • Simulation: Icarus Verilog 13.0 • Datapath: 5-Stage Single-Cycle (CPI = 1)
RISC-V RV32I Single-Cycle Processor | Prince Raj | Verilog HDL & Icarus Verilog

## Slide 2
EXECUTIVE SUMMARY
Project Objectives & Architecture Overview
Bridging theoretical computer architecture with synthesizable hardware implementation
Core Objectives
• Implement 32-bit single-cycle processor core in Verilog HDL • Support RV32I R-type, I-type, LW, SW, and BEQ instructions • Validate design using automated self-checking testbenches • Create interactive demonstrator tool for live hardware execution
Why Single-Cycle Architecture?
• CPI = 1: Every instruction executes in exactly 1 clock cycle • Simplicity: No pipeline hazards, stalls, or forwarding units • Foundation: Establishes baseline dataflow for multi-cycle and pipelined cores
RISC-V RV32I Single-Cycle Processor | Prince Raj | Verilog HDL & Icarus Verilog

## Slide 3
INSTRUCTION SET ARCHITECTURE
RISC-V RV32I Instruction Formats
Regular 32-bit instruction layouts designed for efficient hardware decoding
Format Specifications
• R-Type: [funct7][rs2][rs1][funct3][rd][opcode] -> add, sub, and, or, slt • I-Type: [imm 11:0][rs1][funct3][rd][opcode] -> addi, lw, jalr • S-Type: [imm 11:5][rs2][rs1][funct3][imm 4:0][opcode] -> sw • B-Type: [imm 12|10:5][rs2][rs1][funct3][imm 4:1|11][opcode] -> beq
Hardware Decoding Highlights
• rs1, rs2, rd always occupy identical bit positions • Opcode is always bits [6:0], enabling immediate control generation • 32 registers (x0 to x31) where x0 is hardwired to 0
RISC-V RV32I Single-Cycle Processor | Prince Raj | Verilog HDL & Icarus Verilog

## Slide 4
HARDWARE ORGANIZATION
The 5 Classic Stages of the Single-Cycle Datapath
All stages execute concurrently in combinational logic during each single clock cycle
Stage 1 & 2: Fetch and Decode
1. Instruction Fetch (IF): • PC points to current instruction in Instruction Memory • PC+4 adder prepares sequential next address 2. Instruction Decode (ID): • Control Unit decodes 7-bit opcode • Register File reads rs1 and rs2 combinationally • Immediate Generator reconstructs 32-bit sign-extended constant
Stage 3, 4 & 5: Execute, Memory, Write-Back
3. Execute (EX): • ALU executes arithmetic/logic operation • Calculates Zero flag and branch target (PC + imm) 4. Memory Access (MEM): • Data RAM loads (lw) or stores (sw) 5. Write-Back (WB): • Multiplexer selects ALU result, memory data, or PC+4 into register rd
RISC-V RV32I Single-Cycle Processor | Prince Raj | Verilog HDL & Icarus Verilog

## Slide 5
SUB-MODULE DESIGN
Program Counter & Instruction Memory
Instruction address sequencing and memory fetch hardware
Program Counter (pc.v)
• 32-bit sequential register updating on posedge clk • Asynchronous active-high reset initializing PC to 0x00000000 • Non-blocking assignment (<=) ensures race-free flip-flop synthesis • Latches either PC+4 or branch/jump target address
Instruction Memory (instruction_mem.v)
• 64-word deep ROM holding 32-bit RISC-V instructions • Asynchronous read: assign instr = memory[pc[7:2]]; • pc[7:2] divides byte address by 4 for word index • Supports dynamic hex program loading via $readmemh
RISC-V RV32I Single-Cycle Processor | Prince Raj | Verilog HDL & Icarus Verilog

## Slide 6
SUB-MODULE DESIGN
Register File & Immediate Generator
Dual-read register storage and sign-extending immediate reconstruction
Register File (reg_file.v)
• 32 registers x 32 bits wide • Two combinational read ports (rd_data1, rd_data2) • One synchronous write port triggered on posedge clk when reg_write=1 • Hardwired x0: Reads always return 0, writes to x0 are ignored
Immediate Generator (imm_gen.v)
• Reconstructs scattered immediate bit slices based on opcode • Performs 32-bit sign extension: {{20{instr[31]}}, ...} • Formats handled: I-type (addi, lw), S-type (sw), B-type (beq), J-type (jal)
RISC-V RV32I Single-Cycle Processor | Prince Raj | Verilog HDL & Icarus Verilog

## Slide 7
SUB-MODULE DESIGN
Arithmetic Logic Unit & ALU Control
Core computing engine and hierarchical operation decoding
ALU (alu.v)
• Computes: ADD, SUB, AND, OR, XOR, SLT, Shift Left, Shift Right • Zero Flag: assign zero = (result == 32'b0); Essential for conditional branch evaluation (BEQ)
ALU Control (alu_control.v)
• Multi-level decoding: Main Control sets 2-bit alu_op • Secondary decoder checks funct3 and funct7[5] • Minimizes combinational gate delay across the control path
RISC-V RV32I Single-Cycle Processor | Prince Raj | Verilog HDL & Icarus Verilog

## Slide 8
SUB-MODULE DESIGN
Main Control Unit & Data Memory
Central traffic controller and data storage RAM
Main Control Unit (control_unit.v)
• Decodes opcode[6:0] into 8 control signals: - RegWrite: enables register destination write - ALUSrc: selects Register 2 vs Immediate - MemRead / MemWrite: enables RAM read/write - MemToReg: selects writeback source - Branch / Jump: branch and jump enables
Data Memory (data_mem.v)
• 64 words (256 bytes) RAM addressed by addr[7:2] • Asynchronous combinational read on mem_read=1 • Synchronous write on posedge clk when mem_write=1
RISC-V RV32I Single-Cycle Processor | Prince Raj | Verilog HDL & Icarus Verilog

## Slide 9
TOP CORE INTEGRATION
Top Datapath Multiplexers (riscv_core.v)
Integrating all sub-modules into a unified operational CPU
Branch and Jump Multiplexing
• Branch Target: branch_target = pc_current + imm_out; • Branch Taken: pc_branch_taken = branch & alu_zero; • Next PC MUX: pc_next = (jump || pc_branch_taken) ? branch_target : pc_plus_4;
Operand & Write-Back Multiplexing
• ALU Operand B MUX: alu_operand_b = alu_src ? imm_out : rd_data2; • Write-Back MUX: mem_to_reg selects between ALU result (00), Data RAM read (01), or PC+4 (10)
RISC-V RV32I Single-Cycle Processor | Prince Raj | Verilog HDL & Icarus Verilog

## Slide 10
SIMULATION & VERIFICATION
Automated 11-Instruction Testbench (tb_riscv.v)
Self-checking testbench executed in Icarus Verilog
Test Program Sequence
• PC 0x00: addi x1, x0, 15 -> x1 = 15 • PC 0x04: addi x2, x0, 25 -> x2 = 25 • PC 0x08: add x3, x1, x2 -> x3 = 40 • PC 0x0C: sub x4, x2, x1 -> x4 = 10 • PC 0x10: and x5, x1, x2 -> x5 = 9 • PC 0x14: or x6, x1, x2 -> x6 = 31 • PC 0x18: sw x3, 4(x0) -> Mem[4] = 40 • PC 0x1C: lw x7, 4(x0) -> x7 = 40
Branch Verification & Result
• PC 0x20: beq x3, x7, 8 -> Condition TRUE! • PC 0x24: addi x8, x0, 99 -> SKIPPED (x8 stays 0) • PC 0x28: addi x9, x0, 42 -> TARGET REACHED (x9 = 42) >>> SUCCESS! ALL INSTRUCTIONS VERIFIED <<<
RISC-V RV32I Single-Cycle Processor | Prince Raj | Verilog HDL & Icarus Verilog

## Slide 11
DEMONSTRATION TOOL
Interactive Demonstrator CLI (run_interactive.py)
Real-time user input assembly and hardware simulation tool
Interactive Features
• Accepts user input numbers and operations in terminal • Supports ADD, SUB, AND, OR, XOR, SLT • Assembles machine code dynamically and generates sim/instructions.hex • Runs Icarus Verilog simulation and captures hardware telemetry
Educational Breakdown Displayed
• Decodes instruction into funct7, rs2, rs1, funct3, rd, opcode • Explains the 5-stage physical signal journey • Prints cycle-by-cycle internal Verilog signals • Displays final register values in decimal and hexadecimal
RISC-V RV32I Single-Cycle Processor | Prince Raj | Verilog HDL & Icarus Verilog

## Slide 12
VIVA VOCE PREPARATION
Professor Defense Guide: Key Viva Questions
Authoritative answers for oral examination and project presentation
Architecture & Critical Path
• Q: What is the critical path? A: Load Word (lw). It must traverse Fetch -> Reg Read -> ALU -> Data RAM -> WB Mux -> Reg Write. Clock period must accommodate this. • Q: Why is it called single-cycle? A: Every instruction completes in exactly 1 clock cycle (CPI = 1).
Hardware Decisions
• Q: Why is x0 hardwired to 0? A: Enables compact pseudo-instructions like nop (addi x0, x0, 0) and mv (addi rd, rs, 0) without extra silicon. • Q: Why use non-blocking assignments (<=)? A: Models concurrent hardware flip-flop updates and prevents simulation race conditions.
RISC-V RV32I Single-Cycle Processor | Prince Raj | Verilog HDL & Icarus Verilog

## Slide 13
CONCLUSION
Conclusion & Future Research Roadmap
Summary of achievements and architecture expansion roadmap
Key Outcomes
• Designed and verified synthesizable RV32I single-cycle processor core • Successfully verified all arithmetic, logic, load, store, and branch instructions • Created automated testbenches and live interactive CLI demonstrator tool
Future Enhancements
• 5-Stage Pipelining (IF, ID, EX, MEM, WB) with Hazard Detection • Data forwarding units to eliminate stalls • RV32M Extension: Hardware Multiplier and Divider • L1 Instruction and Data Caches
RISC-V RV32I Single-Cycle Processor | Prince Raj | Verilog HDL & Icarus Verilog